## Slide 1
The System Today: One FGO, Joint Fault Handling, Rolling Integrity
How are estimation, fault exclusion and protection connected in the live UWB–IMU system?
20 Hz UWB / 200 Hz IMU • default LF/LI = 30/30 epochs • committed tag-position PL
Raw measurements drive one incremental FGO and parallel fault monitors; the selector commits at most one native update. A rolling certificate carries state uncertainty, fault
consequences and source/risk identity across marginalization.
Takeaway: A coupled incremental estimator and rolling fault-aware position integrity layer goes beyond a per-epoch
UWB RAIM test.
Source: SC8_RESULTS, Architecture; frozen solver 61907ab; conditional SIM / empirical REAL separated
1/15
Timestamped raw
UWB + IMU
source IDs / noise
Existing discrete
FGO
pre-UWB prepare
IMU preintegration
Unified physical
fault hypothesis
pool
UWB/IMU FDE
Candidate testing
exclude / bridge / repair
Single native commit
iSAM2 actual tag
+ commit receipt
Fault-aware tag PL
Raw set HPL / VPL
around committed tag
UWB slope RAIM screen
Raw IMU fault monitor
Rolling certificate / boundary B_k
p, v, R, ba, bg + historical fault carry
shared source / time-uniform risk
Risk / timeliness / AL
separate availability
gates
T-SIM: conditional raw integrity | T-REAL: engineering FDE only; raw unqualified
Retired raw epochs
Certified boundary B_k
Explicit active FGO / proof: 30 epochs
New epoch k+1
B_k → B_(k+1): state/error, possible faults and source/risk survive; risk horizon ≠ 30 epochs. No second FGO or all-history re-solve.
Notes: • Follow the single estimator path and the two fault-monitor inputs into the hypothesis pool.
• Proof proposal precedes commit; final HPL/VPL are bound to the actual commit receipt and tag center.
• The boundary carries position, velocity, rotation, biases, historical faults and shared source/risk identity.
• The risk horizon is not the 30-epoch explicit window; no second FGO or all-history resolve is required.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 1.

## Slide 2
E00 — What Was Actually Tested, and Which Comparisons Are Valid?
Which datasets, ground truths and algorithm modes support a defensible comparison?
143 registered runs: 130 SUCCESS | 12 RESOURCE_LIMIT | 1 FAIL; 159 attempts + 1 ROS control
Rows identify pre-registered real recordings, rather than six successful examples. The producer-to-estimator lanes keep conditional simulation integrity separate from
empirical real data and overlays.
Takeaway: Comparability comes before APE rankings: Walk reference and STAR input contracts remain open.
Source: SC8_RESULTS, E00; frozen solver 61907ab; conditional SIM / empirical REAL separated
2/15
T-SIM
Registered physical law → O-FULL / O-NOFDE
→ Known truth; conditional PL
T-REAL
Original recordings → O-FDE-ENG /
O-ENG-NOFDE
→ CAL disclosure; raw unqualified
T-SEMI
Real + fixed overlay → Same engineering paths
→ Injected label only; no raw PL
ID
Recording
Duration
Physical reference / boundary
R1
ISAS-Walk2
76.09 s
tracker→IMU/tag OPEN; proxy
R2
ISAS-Walk3
81.66 s
same reference OPEN
R3
Own Vicon, no obstacle
73.39 s
GT-assisted segmented CAL/TEST
R4
Own Vicon, obstacle
11.39 s
GT-assisted; short recording
R5
STAR loop-3d-z_s3
150.10 s
gyro/rig input convention OPEN
R6
STAR loop-2d-fast_s3
55.40 s
same input concern
SFUISE: official rejection ON; ONLINE causal; FINAL same-run revised history.
Notes: • SUCCESS is a process exit status, not proof of complete input or output coverage.
• Simulation is the only registered source with conditional raw qualification.
• Real recordings use O-FDE-ENG / O-ENG-NOFDE; semi-synthetic labels concern the added fault only.
• Own-Vicon calibration uses a disclosed segmented TEST-involved fit; SFUISE official rejection remains enabled.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 2.

## Slide 3
E01 — Healthy Simulation: Good Accuracy Under the Declared Model
How accurately does the coupled pipeline localize without imposed faults?
O-FULL tag APE RMSE 0.0487176–0.0526469 m; default timing / timely-spatial profile passes 3/3
Each point is one independent seed; lower world-frame tag APE is better, without trajectory alignment. SFUISE uses sensor-only initialization, while ours receives an
independently noisy initial observation: this is not an optimizer-only comparison.
Takeaway: The healthy pipeline delivers approximately 5 cm tag RMSE in the registered simulated model.
Source: SC8_RESULTS, E01; frozen solver 61907ab; T-SIM: conditional tag-position PL
3/15
Full path / model
Observed result
Tag APE RMSE (m)
0.0487176–0.0526469
Body ARE RMSE
0.0778–0.1454 rad
Seed20 core / sink P95
23.73 / 23.89 ms
Study limits
40 / 50 ms; timely ≥95%
Per-run output-stamp scoring.
FULL / NOFDE: 600 states each.
SFUISE: 300 online; 298 valid final.
Final history is not an online gain.
Notes: • All three fixed healthy seeds are shown, without seed selection or fitted alignment.
• FULL and NOFDE coincide on the healthy source; SFUISE online and final are distinct views.
• Final history excludes the support-invalid bootstrap prefix; it is neither causal nor a full batch optimum.
• The approximate five-centimeter result is conditional on the registered simulation and initialization information.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 3.

## Slide 4
E02 — Real-Data Validation Is Currently an Interface Problem
Which real-data comparisons can we physically interpret?
Walk physical APE / ARE / RPE = NA; STAR input validation OPEN; own Vicon is GT-assisted
Traces show the frozen own-Vicon TEST output and height reference, with its GT-assisted calibration disclosed. The matrix separates physically unresolved Walk references
and STAR input conventions from conditional empirical scoring.
Takeaway: Apparent algorithm failures cannot yet be separated from missing physical frame and timing validation.
Source: SC8_RESULTS, E02; frozen solver 61907ab; T-REAL: empirical, raw unqualified
4/15
Family
Usable evidence
Open boundary
Walk
R1/R2
Time coverage;
proxy diagnostic
Tracker–body/tag
reference
Own
R3/R4
Empirical TEST;
CAL disclosed
TEST-involved fit; not
blind
STAR
R5/R6
Frozen-interface
behavior
Gyro/rig convention;
no intrinsic ranking
R3 FULL: no complete TEST trajectory.
STAR R5 S-ONLINE APE: 15.85 km.
Input OPEN: no intrinsic-method ranking.
Notes: • Use R3 as an empirical example, not an independently calibrated blind test.
• Its registered TEST begins at 16.678774643 seconds; FULL has no complete TEST trajectory.
• Walk physical APE, ARE and RPE are unavailable despite saved numerical proxy distances.
• STAR kilometer-scale divergence is retained in the frozen report, but the gyro input contract prevents intrinsic method ranking.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 4.

## Slide 5
E02 — Real FDE Execution, Not Nominal Localization, Is the Bottleneck
Can the fault-handling pipeline sustain a complete real recording?
4/6 O-FDE-ENG real runs hit the resource limit; every real raw PL remains unqualified
Bars show coverage of the registered GT TEST grid, with interpolation limited to 100 ms; NA is not zero. This measures emitted-output continuity, not accuracy or raw integrity,
and Walk coverage is temporal only.
Takeaway: The main real-data blocker is FDE execution continuity, beyond nominal FGO data loading.
Source: SC8_RESULTS, E02; frozen solver 61907ab; T-REAL: empirical, raw unqualified
5/15
GT grid
FDE covered/N
NoFDE covered/N
R1
204/3805
3295/3805
R2
236/4083
3483/4083
R3
NA
16602/16617
R4
1591/3344
2741/3344
R5
505/35342
34861/35342
R6
723/12993
12701/12993
Walk: temporal proxy grid only.
R3 FULL has no saved TEST output.
Rates differ from commit/attempt rate.
Notes: • The denominator is each original GT TEST grid within IMU source bounds, not successful matches or commit attempts.
• Walk percentages describe time coverage only; the physical reference is unresolved.
• The R3 FULL TEST coverage is unavailable and must not be drawn as a zero bar.
• Four of six engineering FULL runs hit the registered resource stop; all real raw PL remains unqualified.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 5.

## Slide 6
E03 — FDE Benefits Are Fault-Dependent, Not Uniformly Positive
Does FDE actually improve position and attitude accuracy?
OFF − ON: positive is improvement; negative is degradation; all three seeds remain visible
Each point is a matched seed; positive OFF−ON means FDE reduced RMSE, while negative values show degradation. Position improvement cannot cancel worsening body
attitude, particularly under accel or gyro faults.
Takeaway: Accel/joint positioning improves, but gyro-only accuracy and state recovery remain unresolved.
Source: SC8_RESULTS, E03; frozen solver 61907ab; T-SIM: conditional tag-position PL
6/15
Fault
ΔAPE (m)
ΔARE (rad)
UWB
-0.007908
+0.05806
Accel
+0.092363
-1.13562
Gyro
-0.067733
-1.23141
Joint
+0.114792
+0.20435
Black ticks are seed means.
Accel: better position, worse attitude.
Gyro: both means deteriorate.
Joint: attitude gain varies by seed.
Notes: • Three independently registered seeds per fault class supply the matched ON/OFF gains.
• UWB-only is not uniformly positive; accelerometer positioning gains accompany worse attitude.
• Gyro-only has a large negative seed and negative mean position and attitude gains.
• Joint-fault mean attitude gain hides per-seed variation; no significance claim is made from three seeds.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 6.

## Slide 7
E03 — Real Isolation Can Still Be Followed by Estimation Drift
What happens before, during and after a detected joint fault?
T-SIM SC8-J / seed 20261020: actual prior repair + bridge + rejoined receipts; accuracy is separate
Bands mark source-level injections and receipt rows mark actual detection, isolation, prior repair and rejoined state. The APE axis is linear below 0.1 m and logarithmic above;
a successful transaction does not certify state-error recovery.
Takeaway: Post-FDE state consistency and recovery determine net accuracy; isolation alone is insufficient.
Source: SC8_RESULTS, E03; frozen solver 61907ab; T-SIM: conditional tag-position PL
7/15
Source /
event
Magnitude / receipt
UWB bias
+2.25 m / 3 epochs
Raw accel
+20 m/s² / 500 ms
First FD /
bridge
Epoch 121 / 121
First rejoin4
Epochs 141–144
Burgundy: accel pulse.
Teal: UWB pulse.
Rejoined is a persistent state,
not an accuracy certificate.
Notes: • The title uses real isolation to mean actual native transactions; this example is T-SIM, not a real recording.
• The exact stream is SC8-J, seed 20261020, 600 epochs.
• The raw accel pulse is 20 m/s² for 500 ms and UWB bias is 2.25 m for three epochs.
• Rejoined is a persistent state flag; episode success requires actual prior replacement, bridge and consecutive post-bridge rejoined commits.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 7.

## Slide 8
E04 — Horizontal Stanford:
Conservative Bounds, Conditional Coverage
How do horizontal position errors relate to the emitted HPL?
77,131 qualified T-SIM receipts overall; observed H/V underbounds = 0; correlated samples ≠ risk trials
HPE is horizontal and HPL vertical; darker teal log-count bins have more timely samples, and points above dashed y=x are empirically covered. Gray bins are late (excluded
from timely availability); dotted lines mark research ALs (2/5/10 m), and zero correlated violations do not establish empirical 10^-6 risk.
Takeaway: Horizontal bounds cover the registered errors but remain much wider than the observed error.
Source: SC8_RESULTS, E04; frozen solver 61907ab; T-SIM: conditional tag-position PL
8/15
Notes: • The Stanford panels use actual histogram counts for the registered E01/E03 main cases.
• Overall qualified receipt total includes other experiments and must not be confused with this figure denominator.
• An HPL above HPE is coverage, whereas an HPL above HAL is unavailable at that alert limit.
• The conditional theorem comes from the declared source event, not independence of these correlated observations.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 8.

## Slide 9
E04 — Vertical Stanford: Availability Depends on the Application AL
Why can a centimeter-level estimate still be unavailable?
Same estimates and PL: research AL (2,3) m gives 3.5–5.667%; (5,5) m gives 99.67–100%
VPE is horizontal and VPL vertical; darker teal bins contain more timely samples, gray bins are late, and bins above dashed y=x have VPL≥VPE. Dotted research ALs (3/5/10
m) test admissibility; the healthy AL comparison changes evaluation only, not estimates or PL, and is not certification.
Takeaway: PL tightness and application availability are distinct from estimator accuracy, especially vertically.
Source: SC8_RESULTS, E04; frozen solver 61907ab; T-SIM: conditional tag-position PL
9/15
HAL / VAL
Joint timely
2/3 m
3.5–5.667%
5/5 m
99.67–100%
O-FULL; 3 independent seeds.
Denominator: all 600 epochs / seed.
No application certification.
Notes: • Vertical bounds can exceed the chosen VAL even when VPE is small.
• Healthy joint availability divides timely H/V-admissible receipts by all 600 planned epochs per seed.
• Research 2/3 and 5/5 meter ALs are post-processing diagnostics and do not alter solver parameters.
• No hardware safety requirement or real-data protection qualification is inferred.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 9.

## Slide 10
E05 — 30 vs 1000 Epochs: When Is a Longer Window Worth It?
Does retaining much more history improve accuracy or integrity enough to justify the cost?
7 unique configurations × 2 streams; common epochs 1101–2100; default core study target = 40 ms
APE uses the same complete 1,000-epoch scoring interval; bubble area denotes sampled RSS, not process peak. LF, LI and recovery replay vary together in the coupled
sweep, so its fault benefit cannot be attributed to PL alone.
Takeaway: Keep 30/30 as the online reference; extend history only when measured recovery benefits justify cost.
Source: SC8_RESULTS, E05; frozen solver 61907ab; T-SIM: conditional tag-position PL
10/15
Same common interval
30/30
1000/1000
Interpretation
Healthy APE (m)
0.04753682
0.04754147
No meaningful gain
Healthy core P95 (ms)
25.096
795.501
Higher measured cost
Fault APE (m)
0.10345833
0.05404642
Benefit in this stream
Notes: • Every plotted configuration ran 2100 epochs and the common scoring interval is 1101 through 2100.
• Coupled LF=LI uses 30, 100, 300, 600 and 1000 actual UWB epochs; 1000 is 50 seconds.
• The fixed LF=300 sweep uses LI=30, 100 and 300, reusing the shared 300/300 result.
• The resource marker is a sampled RSS maximum, not the unknown between-sample peak; larger windows are intentionally allowed to miss real-time targets.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 10.

## Slide 11
E06 — Runtime Breakdown: Fast Simulation, Expensive Real FDE
Where does the computation go, and which timing numbers are comparable?
Core P95 ≤40 ms + sink P95 ≤50 ms + timely spatial ≥95%; two E06 serial confirmations pass
Curves show measured whole-service latency; solid is core and dashed is sink, while stacked bars contain additive exclusive means. Stage P95s are not additive, and
SFUISE buffering/software-clock timing represents different capabilities.
Takeaway: The small-window simulated full path meets study P95 targets; current real engineering FDE does not.
Source: SC8_RESULTS, E06; frozen solver 61907ab; conditional SIM / empirical REAL separated
11/15
Run / capability
Core P95 (ms)
Sink P95 (ms)
Boundary
E01 H / seed20 FULL
23.726
23.893
Full service
E06 J / seed20 FULL
24.893
25.162
Full service
E01 H / seed20 NOM
2.100
2.303
Nominal only; no matched PL
E02 real O-FDE-ENG
up to 13099.0
up to 1.14e+06
Measured prefix; 4/6 resource-limited
Notes: • Core and sink nearest-rank P95 targets remain 40 and 50 milliseconds; timely spatial fraction must also exceed 95 percent.
• The healthy seed20 main E01 profile and the E06 joint repeat have distinct run IDs.
• The nominal-only two-millisecond path lacks the full integrity capability and is not a like-for-like speed claim.
• All measurable slow and abort frames remain; censored suffixes have no imputed timing and no complete-stream throughput claim.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 11.

## Slide 12
E07 — Ablations: Which Integrity Components Actually Matter?
Are rolling constraints and recovery logic causally necessary, or just complexity?
Removing support/joint constraints widens PL; the old G2 numerical candidate commits 0/80
Cells show actual values and signed changes from matched FULL; red means increase and blue means decrease. G2 has no qualified output, so APE/PL are NA; the
joint/sample0 switch also removes support and cannot isolate both effects.
Takeaway: Set constraints and geometry-aware numerical recovery have measurable effects; failures remain visible.
Source: SC8_RESULTS, E07; frozen solver 61907ab; T-SIM: conditional tag-position PL
12/15
M — same center
Old/new PL at one committed tag center: a
tightening witness.
A — full trajectory
Changing fault support can change the
subsequent state trajectory.
P — performance
Whole-service measurements; do not sum
module percentiles.
G2: 0/80; epoch1 abort = 4.874 ms.
APE / PL: NA; no common valid baseline.
Joint + support is a combined switch.
Notes: • M means same committed center, A means full trajectory comparison and P means performance.
• Disabling terminal support reverts to a valid conservative box.
• The joint/sample0 ablation is a combined joint-plus-support reversion, not two independently isolated effects.
• G2 disables dedicated numerical recovery and commits zero of eighty epochs; its measured abort cost is retained in the report.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 12.

## Slide 13
E08 — Long-Run Integrity:
Healthy Complete, Repeated-Fault Case Censored
Does the full pipeline sustain 10,000 epochs and process the last injected fault?
All three processes exit SUCCESS; actual FULL L1 coverage is 7171/10000, not full completion
Curves stop at actual committed output; a blank FULL suffix is unprocessed data, not zero error. Vertical marks are scheduled faults, and the final episode beyond epoch 7171
was not verified by FULL.
Takeaway: Continuous recovery at scale is unproven: FULL stops where the no-FDE route continues.
Source: SC8_RESULTS, E08; frozen solver 61907ab; T-SIM: conditional tag-position PL
13/15
Run
Committed /
plan
Queue
peak
L0 FULL
5000/5000
13
L1 FULL
7171/10000
80
L1 NOFDE
10000/10000
15
FULL L1: 2,829 refused epochs.
The final scheduled fault is unverified.
Slots grow; bounded active window
does not mean constant total memory.
Notes: • Process SUCCESS does not imply the ten-thousand-epoch FULL plan completed.
• The producer released the full schedule but queue delivery and actual commits ended early for FULL.
• NOFDE continues to the final scheduled episode, but it implements a different fault-handling policy.
• Slots grow with time despite a bounded active state window; there is no constant-memory or perpetual full-state observability claim.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 13.

## Slide 14
Synthesis — What We Have Demonstrated, and What Remains Open
Which claims can we defend in a paper today?
Demonstrated: conditional method + measured simulation results; not hardware-qualified real integrity
Each row pairs a defensible claim with direct evidence and its limiting assumptions. Mathematical containment, empirical error, execution continuity and application
certification answer different questions.
Takeaway: The strongest current contribution is conditional rolling fault-aware position integrity; real execution remains
open.
Source: SC8_RESULTS, Synthesis; frozen solver 61907ab; conditional SIM / empirical REAL separated
14/15
Defensible claim
Direct SC8 evidence
Boundary / not established
Conditional rolling position PL
77,131 qualified receipts; 0 observed
underbounds
Registered source/noise/fault law only; correlated
observations
Healthy tag positioning ≈5 cm
3 fixed independent simulation seeds
Different initialization information from SFUISE
FDE benefit is fault-specific
Accel/joint position gains; gyro regression
Attitude / late recovery can deteriorate
Real comparison remains incomplete
Walk/STAR interface gaps; real FDE censoring
Engineering empirical results; no raw real
qualification
Default small window justified
25.096 → 795.501 ms healthy core P95
Longer lag helps this fault stream; not generally
real-time
Additional gaps: SFUISE velocity/bias export; invalid history prefix; weak-UWB and S1/S2 studies omitted.
Notes: • The 77131 receipts span correlated scenarios and windows, rather than independent risk trials.
• State estimation, integrity validity, deadline passage and application availability are distinct results.
• Real calibration, engineering execution, historical export support and missing SFUISE state metrics remain explicit gaps.
• Weak-UWB amplitude and S1/S2 bias studies were not registered and are not filled with older SC7 data.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 14.

## Slide 15
Questions for the Advisor — Decisions Needed Before the Next Study
Which scope, resources and priorities should guide the next study?
Proposed next action: close independent calibration → stabilize real FDE → limited newly frozen rerun
The four questions request concrete decisions on scope, calibration resources, recovery priorities and application requirements. The next protocol should follow those
decisions before a limited, newly frozen rerun.
Takeaway: Requested outcome: agree on the paper scope, calibration resource owner and research priority order.
Source: SC8_RESULTS, Decisions; frozen solver 61907ab; conditional SIM / empirical REAL separated
15/15
1. Publication scope
Should the near-term paper focus on the conditional rolling raw
position PL + joint FDE architecture, with honest
execution/real-data limitations, or is physically qualified real-data
integrity required before submission?
Decision: theory + qualified simulation first, or hardware validation first.
2. Independent calibration resources
Can we obtain independent tracker↔IMU/body↔tag 6-DoF
extrinsics, timing and anchor-world references, or collect a new
calibration sequence with three-axis motion and independent
held-out TEST?
Decision: identify the hardware/protocol owner and available sensors.
3. State recovery or execution continuity
Should we prioritize explaining and fixing gyro-induced attitude
degradation / long-term state recovery, or first make engineering
FDE process complete real recordings within a bounded
resource budget?
Decision: algorithmic research priority or engineering qualification
priority.
4. Application integrity requirements
For the intended deployment, what HAL / VAL, TTA, covered
fault classes and failure action should determine meaningful
protected availability?
Decision: target application and first defensible safety requirements.
Notes: • Ask for a near-term publication scope rather than an abstract endorsement.
• Identify an owner for independent extrinsics, clocks and held-out calibration data.
• Choose whether state-recovery research or bounded engineering execution comes first.
• Agree on application HAL, VAL, TTA, covered faults and failure action before the next protocol.
Frozen solver: 61907ab417450d317e443e4ff10f2cce062deabe. Entry HEAD: fa5b3dc9ffe3c88492352491d79ba022f373bfb5. Result status: SC8_EVALUATED_WITH_EXECUTION_GAPS.
Figure provenance: FIGURE_SOURCES.json; metric details: NUMERICAL_CLAIMS.json; slide 15.